## Slide 1
Steelwork Design: Joint Connections
Module CON4334 - Chapter 2
Bolted & Welded Connections

## Slide 2
1. Connection Fundamentals: Bolts vs. Welds
Structural Purpose:
Safely transfer internal actions (Tension, Shear, Moments) between structural members.
Bolted Connections:
Ordinary clearance bolts (Grades 4.6 & 8.8) or Friction Grip (HSFG) bolts.
Key Advantage: Fast, straightforward site assembly without special equipment.
Welded Connections:
Fillet welds (corner joints) & Butt welds (groove joints).
Key Advantage: Neat appearance, compact details, and continuous structural behavior.

## Slide 3
2. Bolted Joints: Hole Clearance & Layout Rules
Standard Clearance Holes:
Bolt diameter (d) <= 24 mm: Hole diameter = d + 2 mm
Bolt diameter (d) > 24 mm: Hole diameter = d + 3 mm
Pitch & Gauge Spacing Limits:
Parallel to load direction (Min Pitch): 2.5 * d
Perpendicular to load direction (Min Gauge): 3.0 * d
Maximum Spacing: Lesser of 12 * t or 150 mm (t = thinner plate thickness)
End & Edge Distances:
Essential to prevent end tear-out failure and ensure adequate bearing area.

## Slide 4
3. Bolted Connections: 5 Core Failure Modes
1. Shear Failure of Bolt Shank:
- Pure shear across single or double shear planes (Ps = ps * As)
2. Bearing Failure on Plate/Bolt:
- Local crushing between bolt shank and plate hole (Pbb = d * tp * pbb)
3. Tension Rupture of Connected Plate:
- Net sectional area yielding/rupture across bolt hole line (Ae = Ke * an)
4. End Shear Tear-Out:
- Tearing of plate end due to inadequate end distance
5. Block Shear Failure:
- Combined shear along bolt lines and tension rupture across end line

## Slide 5
4. Welded Connections: Geometry & Types
Fillet Welds:
Triangular profile in corner joints.
Effective Throat Thickness (a): a = 0.7 * Leg Length (s)
Effective Weld Length: L_effective = Full Length - 2 * s
Butt Welds:
Groove welds achieving full or partial penetration.
Full-penetration butt weld capacity equals parent metal strength.
Non-Destructive Testing (NDT):
Visual inspection, liquid penetrant, magnetic particle, ultrasonic, and X-ray.

## Slide 6
5. Welded Connections: Design Capacity
Simplified Method Capacity Formula:
Weld Strength per mm = 0.7 * Leg Length (s) * Design Weld Strength (pw)
Example (6 mm fillet weld, Grade S355 steel, pw = 250 N/mm2):
- Unit Capacity = 0.7 * 6 * 250 / 1000 = 1.05 kN/mm
Critical Detailing Rules:
Minimum Effective Length: Greater of 4 * Leg Length or 40 mm
End Returns: Continued around corners by at least 2 * Leg Length
Lap Joint Overlap: Minimum 5 * t or 25 mm

## Slide 7
6. Eccentric Connections: Combined Stresses
In-Plane Loading (Direct Shear + Torsion):
Direct Shear (Fs): Distributed equally among all bolts
Torsion Load (FT): Proportional to radial distance from center of gravity
Resultant Load: FR = sqrt(Fs2 + FT2 + 2 * Fs * FT * cos(phi))
Out-of-Plane Loading (Direct Shear + Tension):
Direct Shear (Fs): Uniformly split per bolt
Tension Force (FT): Rotates around bottom bolt line
Interaction Criteria: (Fs / Ps) + (FT / Pnom) <= 1.4

## Slide 8
7. Student Problem-Solving Workflow
1. Calculate Factored Ultimate Load:
- Pu = 1.4 * Dead Load + 1.6 * Imposed Load
2. Fastener / Weld Capacity Check:
- Verify single/double shear, bearing, bolt tension, or weld throat capacity.
3. Plate Capacity Check:
- Check tension capacity on gross section and effective net section (Ae).
4. Layout & Detailing Check:
- Ensure pitch, edge distance, gauge, and end returns meet code limits.