## Slide 1: Steel Beam Design (Chapter 3)

## Slide 2: Learning Objectives
Understand effective length, lateral/torsional restraints, and destabilizing load effects.
Calculate design loads for various limit states.
Produce valid designs for simply supported steel beams
- Section classification
- Shear capacity & moment capacity
- Lateral-torsional instability & buckling resistance
- Deflection checks, web buckling, and web bearing resistance

## Slide 3: Beam Categorization by Restraint
1. Fully Restrained Beams (Clause 8.2):
- Compression flange fully restrained (e.g., concrete slabs supporting floors).
- Lateral restraining force must resist >= 2.5% of maximum factored compression force.
2. Beams Restrained at Intervals (Clause 8.3):
- Subject to Lateral-Torsional Buckling (LTB) between restraints.
- Requires checking segment effective lengths and buckling resistance moments (Mb).

## Slide 4: Cross-Section Classification
Class 1 Plastic: Can develop full plastic moment with high rotation capacity.
Class 2 Compact: Can develop full plastic moment but limited rotation capacity.
Class 3 Semi-Compact: Develops elastic moment; local buckling prevents full plastic moment development.
Class 4 Slender: Local buckling occurs before development of full elastic moment; requires effective properties.
Slenderness parameter: epsilon = Sqr(275 / py).

## Slide 5: Shear Capacity Check (Clause 8.2.1)
Shear Capacity Formula:
Vc = (py * Av) / Sqr(3) >= V
Where Av depends on section type (e.g., tD for rolled I/H and channels, 2td for RHS).
Shear interaction rule:
- If shear load V <= 0.6 Vc, shear effect on bending capacity is small and ignored.
- If V > 0.6 Vc, high shear provisions apply (Clause 8.2.2.2).

## Slide 6: Moment Capacity (Mc) Guidelines
Low Shear (V <= 0.6 Vc):
- Class 1 & 2: Mc = py * S <= 1.2 * py * Z
- Class 3: Mc = py * Z or py * Seff
- Class 4: Mc = py * Zeff or pyr * Z
High Shear (V > 0.6 Vc):
- Class 1 & 2: Mc = py * (S - rho * Sv) <= 1.2 * py * (Z - rho * Sv / 1.5)
- Where rho = (2 * V / Vc - 1)^2.

## Slide 7: Web Bearing & Web Buckling (Clause 8.4.10)
Web Bearing Capacity (Pbw):
- Pbw = (b1 + nk) * t * pyw
- Dispersion of 1:2.5 to root radius line (k = T + r for rolled sections).
Web Buckling Resistance (Px):
- Applies when flanges are restrained against rotation and lateral movement.
- Px = (25 * epsilon * t / Sqr((b1 + nk) * d)) * Pbw (for ae >= 0.7d).

## Slide 8: Lateral-Torsional Buckling (LTB)
Applies to beams not fully restrained along the compression flange.
Check requirement: mLt * Mx <= Mb and Mx <= Mcx.
Equivalent slenderness: lambda_lt = u * v * lambda * Sqr(beta_w).
Buckling resistance moment: Mb = pb * Sx (for Class 1/2 sections).
Destabilizing loads: Multiply effective length LE by a factor of 1.2.

## Slide 9: Restrained Beam Design Workflow
1. Determine dead loads and imposed loads.
2. Calculate factored design moment (Mx) and shear force (V).
3. Estimate member size using Sx = Mx / py.
4. Determine section classification.
5. Check bending and shear capacities.
6. Check web buckling, web bearing, and deflection limits.

## Slide 10: Unrestrained Beam Design Workflow (LTB)
1. Calculate factored loads, moments, and shears.
2. Estimate member size (heavier section usually required since pb < py).
3. Classify section and identify normal vs. destabilizing load.
4. Calculate effective length LE and slenderness lambda = LE / ry.
5. Determine equivalent slenderness lambda_lt and read buckling strength pb from Table 8.3a.
6. Check mLt * Mx <= Mb (Mb = pb * Sx).

## Slide 11: Summary & Tips
Always verify whether the compression flange is fully restrained or restrained at intervals.
Pay careful attention to local section classification before assigning moment capacity formulas.
Do not forget serviceability limit state checks (deflection limits, e.g., L/360 for brittle finishes).
Reference relevant clauses from the HK Code of Practice for Structural Use of Steel.