## Slide 1: Steel Column Design (CON4334)
Chapter 4: Understanding Content, Effective Lengths, and Member Capacity

## Slide 2: Learning Objectives
Understand the concept of effective length and section classification.
Produce valid designs for steel columns under axial force only.
Evaluate simple and continuous construction steel columns under combined axial force and moments.

## Slide 3: 1. Compression Members & Effective Length
Buckling Resistance: Depends on slenderness ratio (Lambda = L_E / r).
Effective Length (L_E): Product of factor K and actual length L (L_E = K * L).
Restraints: Dependent on rotational and positional boundary restraints (Table 8.6).
Compressive Resistance Formula: P_c = A_g * p_c (Applicable to plastic, compact, and semi-compact sections).

## Slide 4: 1.2 Multiple Strut Tables
Compressive Strength (p_c): Depends on section type, design strength (p_y), slenderness (Lambda), and buckling curve.
Strut Curves (Table 8.7): Categorized into curves a, b, c, d based on cross-section geometry and residual stresses.
Tables 8.8(a) to (d): Provide design strength values in N/mm^2 for different steel grades (S275, S355, S460).

## Slide 5: 2. Combined Axial Force & Moments (Clause 8.9)
Dual Verification: Columns must be checked for both cross-section capacity and member buckling resistance.
Cross-Section Capacity Check (Cl. 8.9.1):
(F_c / (A_g * p_y)) + (M_x / M_cx) + (M_y / M_cy) <= 1
Member Buckling Resistance (Cl. 8.9.2): Uses interaction equations taking P-Delta-delta effects into account.

## Slide 6: 2.3 & 2.4 Frame Classification & Amplification
Non-Sway Frames: Lambda_cr >= 10 (P-Delta effects can be ignored).
Sway Frames: 5 <= Lambda_cr < 10.
Sway Ultra-Sensitive Frames: Lambda_cr < 5 (requires second-order advanced analysis).
Moment Amplification Factor: lambda_cr / (lambda_cr - 1) accounts for second-order lateral deflections.

## Slide 7: 3. Columns in Simple Construction
Assumptions: Beams are fully loaded and simply supported; all equivalent moment factors (m) are set to 1.0.
Equivalent Slenderness for Lateral-Torsional Buckling: Lambda_LT = 0.5 * (L / r_y) (where L is storey height, not L_E).
Multi-Storey Provisions (Cl. 8.7.8): Pattern loading need not be considered; nominal moments derived from reaction eccentricities (larger of 100mm from face or centre of stiff bearing).

## Slide 8: Summary: Column Design Checks
Cross-Section Capacity:
[F_c / (A_g * p_y)] + [M_x / M_cx] + [M_y / M_cy] <= 1 (Identical for simple and continuous construction).
Member Buckling Resistance (Simple Construction):
[F_c / P_cy] + [m_LT * M_LT / M_b] + [m_y * M_y / M_cy] <= 1 ( m values = 1.0 ).
Member Buckling Resistance (Continuous Construction):
Uses specific m factors from Table 8.9 and Table 8.4.

## Slide 9: Design Examples & Learning Resources
Practical Applications Covered in Notes:
- Example 1: Column with pinned ends under axial load.
- Example 2: Column with pinned ends tied in weaker axis.
- Example 3: Column with axial load and moments in simple construction.
- Example 4: Axially loaded column using tributary areas & load reductions.

## Slide 10: References & Useful Links
Reference Code / Books:
- Hong Kong Code of Practice for the Structural Use of Steel 2011.
- Steelwork Design Guide to BS 5950 / HK Code (CON4334 Course Notes).
Recommended YouTube Tutorials:
- Steel Column Design Tutorial (Search: 'Steel Column Design EC3 / BS5950 Workflow')
- Understanding Effective Length & Slenderness in Columns (Search: 'Effective Length Buckling Civil Engineering')