## Slide 1: Structural Steelwork Design
Chapter 1: Fundamentals, Steel Metallurgy & HK Code 2011
CON4334 Civil Engineering
LECTURER: King LAI

## Slide 2: Restructured Learning Roadmap
1. Material & Metallurgy (Steel composition, alloys, fatigue, corrosion, fire)
2. Structural Steel Sections (Rolled UB/UC, Built-up, Cold-formed)
3. Limit State Design Philosophy (ULS vs SLS, Partial Safety Factors)
4. Analysis & Imperfections (P-Delta effects, 0.5% NHF)
5. Section Classification & Deflection Limits (Plastic to Slender, SLS Table 5.1)

## Slide 3: Material & Metallurgy
Steel Composition & Strength:
Iron (~98%) + Carbon (max 0.25%)
Higher Carbon = Higher Strength BUT lower Ductility & Weldability.
Manganese (max 1.6%), Silicon, Phosphorous, Sulphur.
Durability & Fire Protection:
Fatigue: Avoid stress concentration & abrupt section changes.
Corrosion: Galvanizing (Zinc), Weathering Steel, Cathodic Protection.
Fire Protection: Solid, Hollow, or Profile Casings required.

## Slide 4: Steel Section Types
1. Rolled Sections:
- UB (Universal Beams): Bending about major axis
- UC (Universal Columns): Heavy axial compression
- Hollow Sections (CHS, SHS, RHS): High compression & torsion efficiency
2. Built-up & Compound Sections: Plate girders, crane girders, battened/laced members
3. Cold Rolled Sections: Thin gauge Zed, Sigma, Lipped channels for purlins

## Slide 5: Limit State Design Philosophy
Ultimate Limit State (ULS):
Focuses on safety against collapse, yielding, and fracture.
Partial Load Factors (γf > 1.0) account for load peak variations.
oMaterial Factor (γm) reduces nominal strength.
Serviceability Limit State (SLS):
Focuses on daily operational fitness.
Controls excessive deflection, floor vibration, and dynamic sway.
Unity Load Factor (γf = 1.0) under unfactored service loads.

## Slide 6: Factored Load Combinations (HK Code 2011)
1. Dead + Imposed Load:
1.4 Dead Load + 1.6 Imposed Load
2. Dead + Wind / Lateral Load:
1.4 Dead Load + 1.4 Wind Load
3. Combined Dead + Imposed + Wind Load:
1.2 Dead Load + 1.2 Imposed Load + 1.2 Wind Load

## Slide 7: Methods of Structural Analysis
Framing Assumptions:
Simple Design: Pinned connections; core/bracing handles lateral load.
Continuous Design: Rigid moment-resisting connections.
Analysis Rigor (HK Code 2011):
First-Order Analysis: Linear elastic, ignores geometry deformation.
Second-Order Analysis: Captures global sway (P-Δ) and member bow (P-δ) nonlinearities.

## Slide 8: Initial Imperfections & NHF
Key Design Rule: Structures are never 100% plumb.
Global Sway Imperfection: Base sway angle φ = 1/200 rad.
Notional Horizontal Force (NHF): Minimum 0.5% (0.005) of total factored vertical load applied horizontally.
Member Bow Imperfection: e0/L initial curvature tolerance.

## Slide 9: SLS Deflection Limits (Table 5.1)
Beams carrying plaster/finishes: Deflection <= L / 360
General Beams: Deflection <= L / 200
Crane Girders: Deflection <= L / 600
Building Frame Sway Drift: Drift <= H / 500

## Slide 10: Steel Grades & Design Strength
Steel Standards:
BS EN Grades: S275, S355, S460 (py = 275, 355, 460 N/mm?).
GB Chinese Standards: Q235, Q345, Q390, Q420.
Thickness Dependency:
Design strength py drops as element thickness 't' increases.
Width-to-thickness ratio parameter: ε = √(275 / py)

## Slide 11: Cross-Section Classification
Class 1 (Plastic): Plastic hinge forms with high rotation capacity for plastic analysis.
Class 2 (Compact): Reaches plastic moment capacity Mp, but local buckling limits rotation.
Class 3 (Semi-Compact): Extreme fiber yields (py), but local buckling prevents full plastic moment.
Class 4 (Slender): Local buckling occurs prematurely before yielding.

## Slide 12: Questions & Discussion